## Slide 1
Asset-Level Criticality in State DOT RIPs
How DOTs calculate criticality, what data they use, and why statewide asset-level scoring is usually staged.
Main answer
Most scoring is not TAZ-level. It is usually asset, segment, corridor, or project-footprint level.
Practical workflow
Screen corridors first, then refine only high-risk/high-criticality assets.
Data reality
Full bridge + every highway segment scoring is possible, but not efficient as a first pass.
Source: downloaded DOT RIP PDFs and compiled summary workbook in Desktop/dot rip

## Slide 2
What ?Criticality? Usually Means
Criticality is the importance of an asset to system function, emergency access, economy, and community resilience.
Traffic importance: AADT, truck AADT, freight value, functional class, NHS status.
Network importance: redundancy, detour availability, alternate routes, evacuation route status.
Community importance: access to hospitals, emergency facilities, shelters, jobs, transit, freight distribution.
Equity importance: disadvantaged communities, social vulnerability, communities with lower recovery capacity.
Operational importance: route role in statewide mobility, maintenance access, tourism, and incident response.
Planning implication
Criticality is often a consequence/proxy layer. It says: if this asset fails, how bad is the disruption?

## Slide 3
Common Data Used for Asset-Level Criticality
These are the recurring data layers across DOT methods.
Traffic
AADT; truck AADT; congestion/reliability; route class
Freight
Freight network tier; truck flow; intermodal connectors; goods movement value
Network redundancy
Detour length; alternate routes; network density; route redundancy
Emergency access
Evacuation routes; hospitals; fire/EMS; shelters; critical facilities
Equity/community
Social vulnerability; disadvantaged community index; population/job density
Asset/system role
NHS; functional class; bridge/roadway role; tourism; regional/statewide mobility

## Slide 4
States With Explicit Asset / Segment Criticality Methods
These DOTs publish clear criticality criteria or formulas.
MI
Criticality = 25% of total risk
AADT, truck AADT, functional class, NHS, CEJEST disadvantaged communities; asset score 1-4.
UT
Criticality criteria normalized 1-4 and summed equally
System redundancy, AADT, truck AADT, disadvantaged community index, community assets, transit/bike service.
RI
Criticality = Usage/Ops 60% + Socioeconomic 20% + Health/Safety 20%
Scores classified High / Medium / Low by percentile.
NM
Criticality binned High / Medium / Low by percentile
Freight network roads/structures automatically receive High criticality.

## Slide 5
States Using Criticality as Consequence or Proxy
Not always called ?criticality,? but the function is similar.
CO
Criticality map
AADT, redundancy, roadway classification, freight value, social vulnerability, tourism value.
OR
Consequence score
Functional class + AADT/truck flow; combined with exposure in a 1-5 risk matrix.
MN
Traveler impact proxy
Federal functional class estimates travelers affected; network density estimates detour/redundancy.
OH
User cost / detour consequence
Criticality embedded in owner/user cost, detour length, and staff input on critical sites.

## Slide 6
States With Partial or Project-Level Criticality
Useful, but not a fully published asset-level formula.
DE
Roadway segment/project factors
Evacuation routes, essential facilities, AADT, DTC ridership, community size, employment density.
NC
Criticality Map component
Criticality is one part of 3-12 point prioritization; full map formula not in extracted pages.
CA
APR / project prioritization
Users affected, redundancy, mobility/economy/safety benefits, community and critical infrastructure benefits.
IA
Project location criticality
Used with cost effectiveness for candidate project ranking; exact formula not disclosed.

## Slide 7
States Where Criticality Is Planned or Not Published
These should not be treated as confirmed formulas.
CT
Asset-level VAST assessment in development
Exposure, sensitivity, adaptive capacity are planned; no final criticality matrix.
VA
Framework planned
AADT, roadway designation, redundancy, evacuation route, important infrastructure; weights not finalized.
TX
Asset vulnerability exists, criticality formula not published
Evacuation route status and critical assets are used, but no numeric criticality matrix found.
FL / VT
No full asset criticality model in downloaded file
FL is engagement plan only; VT is draft project screening with Yes=1 flags.

## Slide 8
Answer to the Asset-Level Question
You do not need to score every asset in full detail at the start.
Recommended structure
Use a staged screening workflow: broad network screen first, then asset-level refinement only where it matters.
1. Network / corridor screen
Use AADT, truck AADT, functional class, freight, evacuation routes, redundancy, and social vulnerability to find critical corridors.
2. Asset-level refinement
For high-criticality corridors only, add bridge condition, scour, culvert size, pavement condition, hydraulic exposure, replacement cost, and detour cost.
3. Project aggregation
Bundle nearby high-risk assets into candidate projects; rank by resilience benefit, readiness, cost effectiveness, equity, and PROTECT eligibility.

## Slide 9
A Practical Criticality Formula You Could Use
This is a defensible planning-level formula inspired by DOT examples.
Example formula
Criticality Score = 25% Traffic + 20% Freight + 20% Redundancy + 15% Emergency Access + 10% Equity + 10% Strategic Route Role
Traffic: normalize AADT into 1-4 or percentile bins.
Freight: truck AADT, freight network tier, intermodal connector flag.
Redundancy: detour length or network density; less redundancy = higher score.
Emergency access: evacuation route, hospital/fire/EMS/shelter access.
Equity: disadvantaged community or social vulnerability index.
Strategic route role: NHS, functional class, statewide corridor, tourism/economic route.

## Slide 10
Key Takeaways
What to carry forward for a statewide resilience screening method.
Criticality is usually not TAZ-level. It is asset, segment, corridor, or project-footprint level.
Do not fully engineer-score every bridge and every segment first. Use corridor screening to narrow the universe.
AADT, truck AADT, functional class, redundancy, evacuation route, essential facilities, and equity are the most reusable data layers.
The strongest published examples are MI, UT, RI, NM, CO, OR, and OH.
For planning, a normalized 1-4 or percentile-based criticality score is easier to maintain than a complex asset-by-asset model.
Local file: C:\Users\xings\Desktop\dot rip\DOT_RIP_asset_level_criticality_summary.pptx